## Slide 1: AHT: Application-Based Handover Triggering for Saving Energy in Cellular Networks
Di Zhang, Yuezhi Zhou, Xiang Lan,
Yaoxue Zhang, Xiaoming Fu
2018-06-12

## Slide 2: Table of Contents
Motivation
Measurement Studies
AHT: Application-Based Handover Triggering
  Application Classification
  Upward Handover
  Downward Handover
Evaluation Results
Conclusions and Future Works

## Slide 3: Motivation
Mobile devices are ubiquitous and indispensable
  Mobile subscriptions are large and increase fast
  Mobile applications are increasingly popular
Chart: Total Amount (Billions)
| 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017*
World population | 6.79 | 6.87 | 6.96 | 7.04 | 7.13 | 7.21 | 7.3 | 7.38 | 7.47 | 7.55
Mobile subscriptions | 4.03 | 4.64 | 5.29 | 5.89 | 6.26 | 6.66 | 6.996 | 7.184 | 7.51 | 7.74
Mobile broadband subscriptions | 0.422 | 0.615 | 0.807 | 1.184 | 1.55 | 1.959 | 2.66 | 3.297 | 3.864 | 4.22
Source: ITU World Telecommunication / ICT Indicators database
Note: *Estimate
Chart: Total APP (Ten Thousands)
| 43252 | 43070 | 42887 | 42705 | 42522 | 42339 | 42156 | 41974 | 41791 | 41609 | 41426 | 41244 | 41061 | 40878 | 40695 | 40513 | 40330
Number of App | 3248252 | 3185495 | 3110143 | 3025251 | 2411366 | 2089293 | 1744717 | 1449591 | 1162009 | 1041187 | 849453 | 687999 | 553852 | 445586 | 358662 | 279856 | 208897
Source: http://www.pocketgamer.biz

## Slide 4: Motivation
Battery is a bottleneck of mobile devices
Cellular data communication is a significant source
Chart: Web Browsing (hours)
| Gionee Marathon M5 | Asus Zenfone Max | Xiaomi Redmi 4 Prime | Xiaomi Mi Max | Xiaomi Mi Max 2 | Xiaomi Redmi Note 4 | Oppo F5 | Lenovo P2 | Huawei Mate 8 | Huawei Ascend Mate2
 | 31 | 20.5 | 20 | 19.5 | 19.5 | 18 | 17.5 | 17.5 | 17 | 16.5
Source: http://www.gsmarena.com/battery-test.php3
Chart: Energy Breakdown
| Cellular | CPU | RAM | Graphics | LCD | Backlight | Others
 | 44 | 14 | 4 | 14 | 4 | 7 | 13

## Slide 5: Motivation
Various heterogeneous cellular networks
  GSM, UMTS, LTE, etc.
Miscellaneous applications need data access
  Instant messaging, social networking
There is a barrier between heterogeneous cellular networks and applications

## Slide 6: Measurement Studies
To understand the barrier between heterogeneous cellular networks and applications
Measurement configurations
  Cellular networks
    EDGE, UMTS, and LTE
  Mobile device
    HTC M8 (equipped with a battery fuel gauge)
  Tool
    EnergyTool (http://github.com/dizhang/EnergyTool)
    Get voltage and current from /sys/class/power_supply

## Slide 7: Measurement Studies
Energy consumption with different cellular networks
  An energy state machine exists in each data transmission
EDGE: limited bandwidth  long transmission time
UMTS: long promotion time  high latency
LTE: long tail time  much energy consumed in tail time
EDGE
UMTS
LTE

## Slide 8: Measurement Studies
Energy consumption with different data size
EDGE is difficult to meet the requirements of modern applications.
UMTS is more energy efficient than LTE.

## Slide 9: Measurement Studies
Impact of the cellular network type on applications
Application | Network Type | Time (ms) | Energy (mJ)
Email checking | EDGE | 5626.4 | 4823.6
 | UMTS | 2506.3 | 4537.0
 | LTE | 436.8 | 11474.3
Web page loading | EDGE | 117067.6 | 163917.9
 | UMTS | 5879.4 | 35614.6
 | LTE | 3511.4 | 44425.3
The cellular network type exerts a crucial influence on energy consumption and performance of applications.
There is no direct interaction between heterogeneous cellular networks and various applications, which leads to the high energy consumption of cellular data transmissions.

## Slide 10: AHT: Overall Idea
Divide heterogeneous cellular networks
  high performance networks with high bandwidth
  energy-efficient networks with low energy consumption
Classify various applications
  UX-sensitive ones that affect the user experience
  UX-insensitive ones that do not affect the user experience
An ideal situation
  UX-sensitive data  high-performance network
  UX-insensitive data  energy-efficient network
AHT triggers handovers based on applications

## Slide 11: Challenges
How to determine whether an application is UX-sensitive or UX-insensitive?
  Various users
  Configurable
How to trigger handovers to the high-performance network?
  Reduce the impact of handover delay
How to trigger handovers to the energy-efficient network?
  Reduce the number of back-and-forth handovers

## Slide 12: Application Classification
AHT classifies applications through user preferences
  To meet the requirements of various users
  Configurable
Appropriate default values are set to reduce the complexity of using AHT
  Common UX-sensitive applications are set in default
A whitelist is used to determine UX-sensitive applications
  Applications that are not in the list are regarded as UX-insensitive

## Slide 13: Upward Handover
Upward handover refers to the handover to the high-performance network
Application prediction based handover triggering
  AHT triggers the upward handover before a UX-sensitive application is used based on application prediction
Two problems
  How to predict the next application?
  When to trigger upward handover?

## Slide 14: Upward Handover Decision
Requirements of applications prediction
  Low training overhead
  Adapt to various users and rapidly changing user habits
Prediction by partial match (PPM)
  Use the prefix character sequence to calculate the conditional probability of the next character
Handover decision
  R={a1, …, an} is the UX-sensitive application set, Pnext={a1, …, am} is a set of applications that may be used as the next
  ∃ ai ∈ R, ai ∈ Pnext, and the network is not the high-performance network, AHT prepares to trigger a handover

## Slide 15: Upward Handover Time
Time
…
…
…
…
ui1
ui2
uii
uij
uin
CDF
UI
PPM
The conditional cumulative distribution function of a that a will be used within Δt period
h1
h2
hi
hj
hn
Historical UI probability
To ensure that all historical handovers
for a will be conducted before a is used

## Slide 16: Upward Handover
The upward handover algorithm

## Slide 17: Downward Handover
Downward handover refers to the handover to the energy-efficient network
Immediate handover at the end use of a UX-sensitive application
  Interruption of in-progress data transmission
  Incur back-and-forth handovers
AHT employs an idle timer to trigger handovers to the energy-efficient network
  Similar to the inactivity time in radio resource control protocol

## Slide 18: Downward Handover
The downward handover algorithm

## Slide 19: Performance Evaluation
Data sets and configurations
  Application usage data from the LiveLab in Rice University
  Parameters are obtained through measurement studies
Performance metrics
  Energy consumption
  Number of total handovers
  Proportion of data transmissions with high latency
Comparison
  Pure network: UMTS and LTE
  Auto: signal strength based handover
  Intelli3G: screen status based handover

## Slide 20: Evaluation Results
Energy consumptions of data transmission for different users
Compared with the pure LTE network, AHT saves up to 60.7% and at least 36.9% energy consumption
Compared with Intelli3G, AHT saves up to 32.8% and at least 12% energy consumption

## Slide 21: Evaluation Results
Number of total handovers
Compared with Auto and Intelli3G, AHT reduces the number of handover by an average of 62.3% and 42.4%, respectively

## Slide 22: Evaluation Results
Proportion of data transmissions with delay more than 2 seconds
The proportion of UMTS is the highest
Compared with Intelli3G, AHT increases the proportion by an average of 8.4% due to application prediction errors

## Slide 23: Conclusions and Future Works
AHT: Application-Based Handover Triggering
  Clarify the barrier between heterogeneous cellular networks and applications
  Propose an application-based handover triggering method
  Based on practical application usage traces, we evaluate the performance of AHT and show its better performance
Future Works
  Integrating AHT with existing handover protocols
  Dynamic idle timer

## Slide 24: Thank you!
Q & A